## Slide 1: Low overhead data race detection in large structured parallel applications
PhD Proposal Defense
Simone Atzeni
simone@cs.utah.edu
May 5, 2016

## Slide 2: Thesis Statement Make race checking of large HPC application practical
Combining the best of static and dynamic analysis techniques for data race detection and tailoring the implementation to the actual concurrency structure of structured parallel languages such as OpenMP, we can make data race checking of HPC applications practical.

## Slide 3: Motivation Model and understand scientific phenomena
Climate modeling
Hydrodynamics modeling
Fast-ignition-scale laser simulation

## Slide 4: Motivation Increased adoption of on-node parallelism in HPC
Sequoia
17 PFLOPS
Tianhe-2
33 PFLOPS
Peta-Scale Machines

## Slide 5: Motivation Architectural trends make HPC debugging a greater challenge
OpenMP predominant programming paradigm in HPC
  Explosion of on-node parallelism
  More sources of non-determinism: data races
    Very hard and expensive to debug
Need more capable and scalable tools!

## Slide 6: Motivation OpenMP is widely used in HPC applications
HYDRA – large multiphysics MPI/OpenMP application
Non-deterministic crashes on a threaded version of Hypre library
Above certain optimization levels and certain scales (8K MPI processes)
Suspected data race
Disable OpenMP in Hypre
Cost scientists months …and performance!

## Slide 7: Motivation Gap in High-End computing environment
Data race bugs in multi-threaded environment:
  One of the most notorious sources of unsafe non-determinism
  Identifying them in large OpenMP applications is highly challenging

## Slide 8: State of the art Overview of Data Race Detection Techniques
Static analyses
Dynamic analyses

## Slide 9: State of the art Static Data Race Detection Techniques
Static Analysis
  Reason about all inputs/interleavings
  Very imprecise, many “false positives” and “false negatives” (miss races)
  Very scalable and fast (i.e. no runtime overhead)
Example Tools:
  Intel Static Security Analysis
    Support OpenMP on C/C++ and Fortran

## Slide 10: State of the art Dynamic Data Race Detection Techniques
Dynamic Analysis
  Very precise, no false positives
  Reports races only in branches of the programs that are actually executed
  Very high runtime and memory overhead (5-20x for best tools)
Example Techniques:
  Lockset Algorithm
  Happens-Before Relation
  Hybrid data race detection
    combination of lockset and happens-before relation

## Slide 11: State of the art Dynamic Data Race Detection Tools
Not many OpenMP data race detectors out there!
Commercial tools:
  Intel Inspector XE: Pthread and OpenMP C/C++ and Fortran
  Sun Studio Data-Race Detection Tool: Pthread and OpenMP C/C++
Open-source tools:
  Helgrind (based on Valgrind): Pthread C/C++ and Fortran
  Thread Sanitizer: Pthread C/C++ and Go
High runtime and memory overhead!
100x slower and 50x memory consumption
on HPC application!

## Slide 12: Overall Research Plan Low overhead data race detection for OpenMP
Data race detection technique for large OpenMP applications
  Combine static and dynamic analysis
    Reduce amount of code to analyze at runtime
  Exploit concurrency structure of OpenMP
    More structured than Pthreads progams
      i.e. join of team of threads at the same point
    Avoid pure happens-before relation
      Vector clocks are expensive
Data race checking of HPC applications
accurate
precise
practical

## Slide 13: Overall Research Plan Step-by-step contributions for OpenMP data race checking
Sequential Blacklisting
  Identify sequential code
Data Dependency Analysis
  Identify race free code
Archer v1
  Combine static techniques and existing dynamic analysis
Clock-less runtime algorithm
  Exploit structured OpenMP parallelism
Archer v2
  Embed static techniques with new runtime algorithm

## Slide 14: Static Analysis Blacklisting Sequential Code
Pthreads fork-join parallelism
  Master thread keeps doing its own work while it spawns new threads
  Hard to distinguish sequential from parallel instructions
    Master thread may access shared variables between other threads
    Some threads may join later

## Slide 15: Static Analysis Blacklisting Sequential Code
OpenMP’s structured fork-join parallelism
  Guarantee finding sequential instructions
  Every instruction outside a OpenMP construct is executed by the master thread
  Master thread take part of the parallel team

## Slide 16: Static Analysis Data Dependency Analysis
#pragma omp parallel for
for(int i = 0; i < N; i++) {
a[i] = a[i] + 1;
}
#pragma omp parallel for
for(int i = 1; i < N; i++) {
a[i] = a[i - 1];
}
Loop-carried data dependency analysis:
  Parallel for-loops with no dependencies are race free
  Blacklisting these regions from runtime analysis
No data dependency, code can be excluded from runtime analysis
Data dependency on array access, potentially race therefore checked at runtime

## Slide 17: Archer v1 Combining Static and Dynamic Analysis
LLVM/Clang based tool
LLVM Passes
  Sequential blacklisting
  Polly + custom pass to identify OpenMP for-loops
Custom TSan instrumentation process
  Exploit static analysis result to exclude race free code from runtime analysis

## Slide 18: Archer v1 Combining Static and Dynamic Analysis
TSan data race runtime analysis
Instrumented OpenMP runtime
  Annotations mechanism to communicate TSan runtime about happens-before relations between threads
  Unknown synchronization mechanism (i.e. barriers, criticals, etc.)

## Slide 19: Example Archer Static Analysis at Work

## Slide 20: Example Archer Runtime with Annotated OpenMP Runtime
6 #pragma omp parallel for
7 {
8 for(int i = 0; i < 100; i++)
9 v[i] = v[i] * v[i];
}
11
12 #pragma omp parallel
13 {
14 if (a < 100) {
15 #pragma omp critical
16 a++;
17 }
18 }
Excluded from them runtime check because
it is race free.
WARNING: ThreadSanitizer: data race
Read of size 4 at 0x7fffffffdcdc by thread T2:
#0 .omp_outlined. race.c:14 (race+0x0000004a6dce)
#1 __kmp_invoke_microtask <null> (libomp_tsan.so)
Previous write of size 4 at 0x7fffffffdcdc by main thread:
#0 .omp_outlined. race.c:16 (race+0x0000004a6e2c)
#1 __kmp_invoke_microtask <null> (libomp_tsan.so)

## Slide 21: Archer v1 Accomplished Research
First open source OpenMP data race detector tool
25% speedup while maintaining same or better precision and accuracy than other tools (OmpSCR and AMG benchmarks)
Used by HPC community
Presentation at IPDPS’16

## Slide 22: Clock-less runtime algorithm Exploit structured OpenMP parallelism
OpenMP concurrency model
  Race within parallel region (e.g. 3 and 4)
  Race across parallel regions (e.g. 8 and 5)
  No race between threads that belong to consequent parallel regions (e.g. 3 and 9)
Labeling approach
Limit data race checking only to concurrent threads

## Slide 23: Clock-less runtime algorithm OpenMP Formal Concurrency Model
Definition of OpenMP concurrency structure
  State machine and a set of transition rules
  Rules model the behavior of the OpenMP constructs (e.g. parallel begin and end, barriers, critical sections, loads/stores, etc.)
  “RaceCheck” rule can fire anytime during the state machine execution

## Slide 24: Clock-less runtime algorithm Implementation as Approximation of the State Machine
Corner cases in OpenMP data race checking
Lock-free data structure to model the concurrency structure of a parallel region
Store a representative set of memory accesses (e.g. sampling, etc.)
Perform race checking at barrier checkpoints
Implementation based on OpenMP Tools API (OMPT)

## Slide 25: Timeline Past and future publications
Feasibility of combining static and dynamic analysis for OpenMP data race detection [LLVM-HPC WS/SC’14]
Archer v1 – static analysis and TSan runtime [IPDPS’16]
Clock-less runtime algorithm [POPL’17, PPoPP’17]
Archer v2 – static analysis and clock-less runtime algorithm [PLDI’17, IPDPS’17]

## Slide 26
Questions?